# Explanation of Key Trends - Fine Particulate Matter (PM₁₀)
## Main drivers
Between 1995 and 2019 the total PM10 emissions dropped 41,2%. The Main Drivers for PM₁₀ emissions are Fuel Combustion (NFR 1.A) with 48% of total 1995 emissions and a 57% reduction between 1995-2019 and as a sum the Industrial Processes (NFR 2) (and especially Handling of Bulk Products NFR 2.L therein) with 39% of total 1995 emissions and a 33% reduction between 1995-2019.
Within NFR 1.A, Transport (NFR 1.A.3) produces the biggest part of PM₁₀ emissions. Here, about 75% of 2019 Transport PM₁₀ emissions are produced by Road Transport (NFR 1.A.3.b), half of which is directly caused by fuel combustion (NFR 1.A.3.b.i - iv) and the other half by road abrasion and tyre and brake wear (NFR 1.A.3.b.vi - vii).
PM₁₀ Emissions 1990-2019
Total Emissions (kt)					Trend: latest compared to
1995	2000	2005	2010	2011	2012	2013	2014	2015	2016	2017	2018	2019	1990	last years
2.341	1.804	1.486	1.361	1.273	1.257	1.212	1.174	1.147	1.142	1.147	1.125	1.121	-71,2% / down

PM₁₀ trend by sector